## Slide 1: Question 223.44.1
Can a changing magnetic field create an electric current?
Yes
No

## Slide 2: Question 223.44.2
Can a changing magnetic field create an electric field?
Yes
No

## Slide 3: Question 223.44.3
In order to change the magnetic flux through the loop, what would you have to do?
a) drop the magnet
b) move the magnet upwards
c) move the magnet sideways
d) only (a) and (b)
e) all of the above

## Slide 4: Question 223.44.3
Moving the magnet in any direction would change the magnetic field through the loop and thus the magnetic flux.
In order to change the magnetic flux through the loop, what would you have to do?
a) drop the magnet
b) move the magnet upwards
c) move the magnet sideways
d) only (a) and (b)
e) all of the above

## Slide 5
v
B
I

## Slide 6
z
x
y
Bexternal

## Slide 8: Question 223.44.4
a) tilt the loop
b) change the loop area
c) use thicker wires
d) only (a) and (b)
e) all of the above
In order to change the magnetic flux through the loop, what would you have to do?

## Slide 9: Question 223.44.4
a) tilt the loop
b) change the loop area
c) use thicker wires
d) only (a) and (b)
e) all of the above
Since F = B A cosq , changing the area or tilting the loop (which varies the projected area) would change the magnetic flux through the loop.
In order to change the magnetic flux through the loop, what would you have to do?

## Slide 10: Question 223.44.5
If a North pole moves toward the loop from above the page, in what direction is the induced current?
a) clockwise
b) counterclockwise
c) no induced current

## Slide 11: Question 223.44.5
If a North pole moves toward the loop from above the page, in what direction is the induced current?
a) clockwise
b) counterclockwise
c) no induced current
The magnetic field of the moving bar magnet is pointing into the page and getting larger as the magnet moves closer to the loop. Thus the induced magnetic field has to point out of the page. A counterclockwise induced current will give just such an induced magnetic field.
Follow-up: What happens if the magnet is stationary but the loop moves?

## Slide 12: Question 223.44.6
If a North pole moves toward the loop in the plane of the page, in what direction is the induced current?
a) clockwise
b) counterclockwise
c) no induced current

## Slide 13: Question 223.44.6
Since the magnet is moving parallel to the loop, there is no magnetic flux through the loop. Thus the induced current is zero.
If a North pole moves toward the loop in the plane of the page, in what direction is the induced current?
a) clockwise
b) counterclockwise
c) no induced current

## Slide 14: Question 223.44.7
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
A wire loop is being pulled through a uniform magnetic field. What is the direction of the induced current?
a) clockwise
b) counterclockwise
c) no induced current

## Slide 15: Question 223.44.7
Since the magnetic field is uniform, the magnetic flux through the loop is not changing. Thus no current is induced.
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
A wire loop is being pulled through a uniform magnetic field. What is the direction of the induced current?
a) clockwise
b) counterclockwise
c) no induced current
Follow-up: What happens if the loop moves out of the page?

## Slide 16: Question 223.44.8
a) clockwise
b) counterclockwise
c) no induced current
A wire loop is being pulled through a uniform magnetic field that suddenly ends. What is the direction of the induced current?
x x x x x
x x x x x
x x x x x
x x x x x
x x x x x
x x x x x
x x x x x

## Slide 17: Question 223.44.8
a) clockwise
b) counterclockwise
c) no induced current
A wire loop is being pulled through a uniform magnetic field that suddenly ends. What is the direction of the induced current?
The B field into the page is disappearing in the loop, so it must be compensated by an induced flux also into the page. This can be accomplished by an induced current in the clockwise direction in the wire loop.
x x x x x
x x x x x
x x x x x
x x x x x
x x x x x
x x x x x
x x x x x
Follow-up: What happens when the loop is completely out of the field?

## Slide 18: Question 223.44.9
a) clockwise
b) counterclockwise
c) no induced current
What is the direction of the induced current if the B field suddenly increases while the loop is in the region?
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x
x x x x x
x x x x x
x x x x x
x x x x x
x x x x x
x x x x x

## Slide 19: Question 223.44.9
a) clockwise
b) counterclockwise
c) no induced current
What is the direction of the induced current if the B field suddenly increases while the loop is in the region?
The increasing B field into the page must be countered by an induced flux out of the page. This can be accomplished by induced current in the counterclockwise direction in the wire loop.
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x
x x x x x
x x x x x
x x x x x
x x x x x
x x x x x
x x x x x
Follow-up: What if the loop stops moving while the field increases?

## Slide 20: Question 223.44.10
a) clockwise
b) counterclockwise
c) no induced current
If a coil is shrinking in a magnetic field pointing into the page, in what direction is the induced current?

## Slide 21: Question 223.44.10
The magnetic flux through the loop is decreasing, so the induced B field must try to reinforce it and therefore points in the same direction — into the page. According to the right-hand rule, an induced clockwise current will generate a magnetic field into the page.
a) clockwise
b) counterclockwise
c) no induced current
If a coil is shrinking in a magnetic field pointing into the page, in what direction is the induced current?
Follow-up: What if the B field is oriented at 90° to its present direction?

## Slide 22: Question 223.44.11
If a coil is rotated as shown, in a magnetic field pointing to the left, in what direction is the induced current?
a) clockwise
b) counterclockwise
c) no induced current

## Slide 23: Question 223.44.11
As the coil is rotated into the B field, the magnetic flux through it increases. According to Lenz’s Law, the induced B field has to oppose this increase, thus the new B field points to the right. An induced counterclockwise current produces just such a B field.
If a coil is rotated as shown, in a magnetic field pointing to the left, in what direction is the induced current?
a) clockwise
b) counterclockwise
c) no induced current

## Slide 24
v
B
I

## Slide 25: Question 223.44.12
N
S
N
S
1
2
a) V1 > V2
b) V1 < V2
c) V1 = V2  0
d) V1 = V2 = 0
Wire #1 (length L) forms a one-turn loop, and a bar magnet is dropped through. Wire #2 (length 2L) forms a two-turn loop, and the same magnet is dropped through. Compare the magnitude of the induced voltages in these two cases.

## Slide 26: Question 223.44.12
Faraday’s law:
depends on N (number of loops) so the induced emf is twice as large in the wire with 2 loops.
N
S
N
S
1
2
a) V1 > V2
b) V1 < V2
c) V1 = V2  0
d) V1 = V2 = 0
Wire #1 (length L) forms a one-turn loop, and a bar magnet is dropped through. Wire #2 (length 2L) forms a two-turn loop, and the same magnet is dropped through. Compare the magnitude of the induced voltages in these two cases.

## Slide 27: Question 223.44.13
N
S
N
S
1
2
a) I1 > I2
b) I1 < I2
c) I1 = I2  0
d) I1 = I2 = 0
Wire #1 (length L) forms a one-turn loop, and a bar magnet is dropped through. Wire #2 (length 2L) forms a two-turn loop, and the same magnet is dropped through. Compare the magnitude of the induced currents in these two cases.

## Slide 28: Question 223.44.13
Faraday’s law:
says that the induced emf is twice as large in the wire with 2 loops. The current is given by Ohm’s law: I = V/R. Since wire #2 is twice as long as wire #1, it has twice the resistance, so the current in both wires is the same.
N
S
N
S
1
2
a) I1 > I2
b) I1 < I2
c) I1 = I2  0
d) I1 = I2 = 0
Wire #1 (length L) forms a one-turn loop, and a bar magnet is dropped through. Wire #2 (length 2L) forms a two-turn loop, and the same magnet is dropped through. Compare the magnitude of the induced currents in these two cases.

## Slide 29: Question 223.44.14
A bar magnet is held above the floor and dropped. In 1, there is nothing between the magnet and the floor. In 2, the magnet falls through a copper loop. How will the magnet in case 2 fall in comparison to case 1?
copper
loop
N
S
2
N
S
1
a) it will fall slower
b) it will fall faster
c) it will fall the same

## Slide 30: Question 223.44.14
When the magnet is falling from above the loop in 2, the induced current will produce a North pole on top of the loop, which repels the magnet.
When the magnet is below the loop, the induced current will produce a North pole on the bottom of the loop, which attracts the South pole of the magnet.
A bar magnet is held above the floor and dropped. In 1, there is nothing between the magnet and the floor. In 2, the magnet falls through a copper loop. How will the magnet in case 2 fall in comparison to case 1?
copper
loop
N
S
2
N
S
1
a) it will fall slower
b) it will fall faster
c) it will fall the same
Follow-up: What happens in case 2 if you flip the magnet so that the South pole is on the bottom as the magnet falls?

## Slide 31: Question 223.44.15
a) induced current doesn’t need any energy
b) energy conservation is violated in this case
c) there is less KE in case 2
d) there is more gravitational PE in case 2
If there is induced current, doesn’t that cost energy? Where would that energy come from in case 2?
N
S
2
copper
loop
N
S
1

## Slide 32: Question 223.44.15
a) induced current doesn’t need any energy
b) energy conservation is violated in this case
c) there is less KE in case 2
d) there is more gravitational PE in case 2
If there is induced current, doesn’t that cost energy? Where would that energy come from in case 2?
In both cases, the magnet starts with the same initial gravitational PE.
In case 1, all the gravitational PE has been converted into kinetic energy.
In case 2, we know the magnet falls slower, thus there is less KE. The difference in energy goes into making the induced current.
N
S
2
copper
loop
N
S
1

## Slide 33: Question 223.44.16
A wire loop is being pulled away from a current-carrying wire. What is the direction of the induced current in the loop?
I
a) clockwise
b) counterclockwise
c) no induced current
Notes: [CORRECT 5 ANSWER]

## Slide 34: Question 223.44.16
The magnetic flux is into the page on the right side of the wire and decreasing due to the fact that the loop is being pulled away. By Lenz’s Law, the induced B field will oppose this decrease. Thus, the new B field points into the page, which requires an induced clockwise current to produce such a B field.
I
A wire loop is being pulled away from a current-carrying wire. What is the direction of the induced current in the loop?
a) clockwise
b) counterclockwise
c) no induced current

## Slide 35: Question 223.44.17
What is the induced current if the wire loop moves in the direction of the blue arrow ?
a) clockwise
b) counterclockwise
c) no induced current
I
Notes: [CORRECT 5 ANSWER]

## Slide 36: Question 223.44.17
The magnetic flux through the loop is not changing as it moves parallel to the wire. Therefore, there is no induced current.
I
a) clockwise
b) counterclockwise
c) no induced current
What is the induced current if the wire loop moves in the direction of the yellow arrow ?

## Slide 37
F
B
v

+q

## Slide 38


## Slide 39
v
I
B
Fpull
x
`

## Slide 40: Question 223.44.E1
a) clockwise
b) counterclockwise
c) no induced current
At the moment shown, what direction is the induced current?

## Slide 41: Question 223.44.E2
a) clockwise
b) counterclockwise
c) no induced current
At the moment shown, what direction is the induced current?