## Slide 1: Question 223.34.1
Capacitor C1 is connected across a battery of 5 V. An identical capacitor C2 is connected across a battery of 10 V. Which one has the most charge?
1) C1
2) C2
3) both have the same charge
4) it depends on other factors
+Q
–Q
+Q
–Q
10V
5V
C1
C2

## Slide 2: Question 223.34.1
Since Q = C V and the two capacitors are identical, the one that is connected to the greater voltage has the most charge, which is C2 in this case.
Capacitor C1 is connected across a battery of 5 V. An identical capacitor C2 is connected across a battery of 10 V. Which one has the most charge?
1) C1
2) C2
3) both have the same charge
4) it depends on other factors
+Q
–Q

## Slide 3: Question
An old-fashioned capacitor is made from two metal balls. The capacitor is connected to the battery and the circuit has a switch. What happens when the switch is closed?
The capacitor jumps instantaneously to its maximum charge Q
The capacitor slowly charges at a constant rate to it’s maximum charge Q
The capacitor initially charges quickly but then charges more slowly asymptotically approaching the maximum charge Q
Switch

## Slide 6
Charge built up on the capacitor plate
New charge repelled

## Slide 7: Question 223.34.2
1) increase the area of the plates
2) decrease separation between the plates
3) decrease the area of the plates
4) either (1) or (2)
5) either (2) or (3)
What must be done to a capacitor in order to increase the amount of charge it can hold (for a constant voltage)?
+Q
–Q

## Slide 8: Question 223.34.2
Since Q = C V, in order to increase the charge that a capacitor can hold at constant voltage, one has to increase its capacitance. Since the capacitance is given by , that can be done by either increasing A or decreasing d.
1) increase the area of the plates
2) decrease separation between the plates
3) decrease the area of the plates
4) either (1) or (2)
5) either (2) or (3)
What must be done to a capacitor in order to increase the amount of charge it can hold (for a constant voltage)?
+Q
–Q

## Slide 9: Question 223.34.3
+Q
–Q
A parallel-plate capacitor initially has a voltage of 400 V and stays connected to the battery. If the plate spacing is now doubled, what happens?
1) the voltage decreases
2) the voltage increases
3) the charge decreases
4) the charge increases
5) both voltage and charge change

## Slide 10: Question 223.34.3
Since the battery stays connected, the voltage must remain constant ! Since when the spacing d is doubled, the capacitance C is halved. And since Q = C V, that means the charge must decrease.
+Q
–Q
A parallel-plate capacitor initially has a voltage of 400 V and stays connected to the battery. If the plate spacing is now doubled, what happens?
1) the voltage decreases
2) the voltage increases
3) the charge decreases
4) the charge increases
5) both voltage and charge change
Follow-up: How do you increase the charge?

## Slide 11: Question 223.34.4
A parallel-plate capacitor initially has a potential difference of 400 V and is then disconnected from the charging battery. If the plate spacing is now doubled (without changing Q), what is the new value of the voltage?
1) 100 V
2) 200 V
3) 400 V
4) 800 V
5) 1600 V
+Q
–Q

## Slide 12: Question 223.34.4
Once the battery is disconnected, Q has to remain constant, since no charge can flow either to or from the battery. Since when the spacing d is doubled, the capacitance C is halved. And since Q = C V, that means the voltage must double.
A parallel-plate capacitor initially has a potential difference of 400 V and is then disconnected from the charging battery. If the plate spacing is now doubled (without changing Q), what is the new value of the voltage?
1) 100 V
2) 200 V
3) 400 V
4) 800 V
5) 1600 V
+Q
–Q

## Slide 14: Capacitance of a Cylindrical Capacitor
From Gauss’s Law, the field between the cylinders is
E = 2keλ / r
DV = -2keλ ln (b/a)
The capacitance becomes
b
a

## Slide 15: Capacitance of a Cylindrical Capacitor
From Gauss’s Law, the field between the cylinders is
E = 2keλ / r
DV = -2keλ ln (b/a)
The capacitance becomes
E

## Slide 16
3v
3v
Time
Time
0v
3v
3v
Time
3v

## Slide 17: Drawing Items
Capacitor
Battery
+
-
Capacitor
Battery

## Slide 18: Question
What is the equivalent capacitance of the following circuit?
C1 + C2
C1 - C2
+
-
C1
C2

## Slide 19: Question
What is the equivalent capacitance of the following circuit?
C1 + C2
C1 - C2
+
-
C1
C2

## Slide 20: Question 223.34.5
o
o
C
C
C
Ceq
1) Ceq = 3/2 C
2) Ceq = 2/3 C
3) Ceq = 3 C
4) Ceq = 1/3 C
5) Ceq = 1/2 C
What is the equivalent capacitance, Ceq , of the combination below?

## Slide 21: Question 223.34.5
The 2 equal capacitors in series add up as inverses, giving 1/2 C. These are parallel to the first one, which add up directly. Thus, the total equivalent capacitance is 3/2 C.
o
o
C
C
C
Ceq
1) Ceq = 3/2 C
2) Ceq = 2/3 C
3) Ceq = 3 C
4) Ceq = 1/3 C
5) Ceq = 1/2 C
What is the equivalent capacitance, Ceq , of the combination below?

## Slide 22
+
-
C1
C2

## Slide 23
+
-
C1
C2

## Slide 24: END

## Slide 25
V
Q
Q

## Slide 26: Question 223.34.5.5
Suppose we charge up a capacitor. Is there energy stored in the capacitor?
Yes
No
Maybe

## Slide 27: Question 223.34.5.6
Suppose we charge up a capacitor. If there is energy stored in the capacitor, where did it come from?
Chemical potential energy converted to electrical potential energy
Mechanical energy converted to electrical potential energy
Work being done on charges to put them in place on the capacitor
Pushing the capacitor up hill

## Slide 28
Question 223.34.6
a) double
b) quadruple
c) Be halved
d) Stay the same
If I double the charge on a capacitor, the amount of energy stored in the capacitor will

## Slide 29
Question 223.34.7
a) C1
C2
Neither, they will have the same energy stored
I have two capacitors hooked to a battery. C1 has twice the capacitance of C2. Which capacitor is storing more energy?

## Slide 30
Question 223.34.8
a) On the positive plate
b) On the negative plate
c) In the air inside the capacitor
d) In the electric field in the capacitor
In a charged capacitor, where is the energy stored?