## Slide 1: Question 223.44.12
N
S
N
S
1
2
1) V1 > V2
2) V1 < V2
3) V1 = V2  0
4) V1 = V2 = 0
Wire #1 (length L) forms a one-turn loop, and a bar magnet is dropped through. Wire #2 (length 2L) forms a two-turn loop, and the same magnet is dropped through. Compare the magnitude of the induced voltages in these two cases.

## Slide 2: Question 223.44.12
Faraday’s law:
depends on N (number of loops) so the induced emf is twice as large in the wire with 2 loops.
N
S
N
S
1
2
1) V1 > V2
2) V1 < V2
3) V1 = V2  0
4) V1 = V2 = 0
Wire #1 (length L) forms a one-turn loop, and a bar magnet is dropped through. Wire #2 (length 2L) forms a two-turn loop, and the same magnet is dropped through. Compare the magnitude of the induced voltages in these two cases.

## Slide 3: Question 223.44.13
N
S
N
S
1
2
1) I1 > I2
2) I1 < I2
3) I1 = I2  0
4) I1 = I2 = 0
Wire #1 (length L) forms a one-turn loop, and a bar magnet is dropped through. Wire #2 (length 2L) forms a two-turn loop, and the same magnet is dropped through. Compare the magnitude of the induced currents in these two cases.

## Slide 4: Question 223.44.13
Faraday’s law:
says that the induced emf is twice as large in the wire with 2 loops. The current is given by Ohm’s law: I = V/R. Since wire #2 is twice as long as wire #1, it has twice the resistance, so the current in both wires is the same.
N
S
N
S
1
2
1) I1 > I2
2) I1 < I2
3) I1 = I2  0
4) I1 = I2 = 0
Wire #1 (length L) forms a one-turn loop, and a bar magnet is dropped through. Wire #2 (length 2L) forms a two-turn loop, and the same magnet is dropped through. Compare the magnitude of the induced currents in these two cases.

## Slide 5: Question 223.44.14
A bar magnet is held above the floor and dropped. In 1, there is nothing between the magnet and the floor. In 2, the magnet falls through a copper loop. How will the magnet in case 2 fall in comparison to case 1?
copper
loop
N
S
2
N
S
1
1) it will fall slower
2) it will fall faster
3) it will fall the same

## Slide 6: Question 223.44.14
When the magnet is falling from above the loop in 2, the induced current will produce a North pole on top of the loop, which repels the magnet.
When the magnet is below the loop, the induced current will produce a North pole on the bottom of the loop, which attracts the South pole of the magnet.
A bar magnet is held above the floor and dropped. In 1, there is nothing between the magnet and the floor. In 2, the magnet falls through a copper loop. How will the magnet in case 2 fall in comparison to case 1?
copper
loop
N
S
2
N
S
1
1) it will fall slower
2) it will fall faster
3) it will fall the same
Follow-up: What happens in case 2 if you flip the magnet so that the South pole is on the bottom as the magnet falls?

## Slide 7: Question 223.44.15
1) induced current doesn’t need any energy
2) energy conservation is violated in this case
3) there is less KE in case 2
4) there is more gravitational PE in case 2
If there is induced current, doesn’t that cost energy? Where would that energy come from in case 2?
N
S
2
copper
loop
N
S
1

## Slide 8: Question 223.44.15
1) induced current doesn’t need any energy
2) energy conservation is violated in this case
3) there is less KE in case 2
4) there is more gravitational PE in case 2
If there is induced current, doesn’t that cost energy? Where would that energy come from in case 2?
In both cases, the magnet starts with the same initial gravitational PE.
In case 1, all the gravitational PE has been converted into kinetic energy.
In case 2, we know the magnet falls slower, thus there is less KE. The difference in energy goes into making the induced current.
N
S
2
copper
loop
N
S
1

## Slide 9: Question 223.44.16
A wire loop is being pulled away from a current-carrying wire. What is the direction of the induced current in the loop?
I
1) clockwise
2) counterclockwise
3) no induced current
Notes: [CORRECT 5 ANSWER]

## Slide 10: Question 223.44.16
The magnetic flux is into the page on the right side of the wire and decreasing due to the fact that the loop is being pulled away. By Lenz’s Law, the induced B field will oppose this decrease. Thus, the new B field points into the page, which requires an induced clockwise current to produce such a B field.
I
A wire loop is being pulled away from a current-carrying wire. What is the direction of the induced current in the loop?
1) clockwise
2) counterclockwise
3) no induced current

## Slide 11: Question 223.44.17
What is the induced current if the wire loop moves in the direction of the blue arrow ?
1) clockwise
2) counterclockwise
3) no induced current
I
Notes: [CORRECT 5 ANSWER]

## Slide 12: Question 223.44.17
The magnetic flux through the loop is not changing as it moves parallel to the wire. Therefore, there is no induced current.
I
1) clockwise
2) counterclockwise
3) no induced current
What is the induced current if the wire loop moves in the direction of the yellow arrow ?

## Slide 13: Question 223.45.1
A wire loop is in a uniform magnetic field. Current flows in the wire loop, as shown. What does the loop do?
(1) moves to the right
(2) moves up
(3) remains motionless
(4) rotates
(5) moves out of the page

## Slide 14: Question 223.45.1
There is no magnetic force on the top and bottom legs, since they are parallel to the B field. However, the magnetic force on the right side is into the page, and the magnetic force on the left side is out of the page. Therefore, the entire loop will tend to rotate.
A wire loop is in a uniform magnetic field. Current flows in the wire loop, as shown. What does the loop do?
(1) moves to the right
(2) moves up
(3) remains motionless
(4) rotates
(5) moves out of the page
This is how a motor works !!

## Slide 15
N
S
Slip rings
Brushes

## Slide 16: Question 223.45.2
A generator has a coil of wire rotating in a magnetic field. If the rotation rate increases, how is the maximum output voltage of the generator affected?
1) increases
2) decreases
3) stays the same
4) varies sinusoidally

## Slide 17: Question 223.45.2
The maximum voltage is the leading term that multiplies sin(wt) and is given by e0 = NBAw. Therefore, if w increases, then e0 must increase as well.
A generator has a coil of wire rotating in a magnetic field. If the rotation rate increases, how is the maximum output voltage of the generator affected?
1) increases
2) decreases
3) stays the same
4) varies sinusoidally

## Slide 18
a/2
B

A

## Slide 23: Question
What is the average value for the voltage generated by our generator?
0

## Slide 28
u

## Slide 29
u

## Slide 30
N1
N2
Iron Core
V1
V2
Alternating
Current Source
Switch
R

## Slide 31: Question 223.45.3
120 V
What is the voltage across the lightbulb?
1) 30 V
2) 60 V
3) 120 V
4) 240 V
5) 480 V

## Slide 32: Question 223.45.3
The first transformer has a 2:1 ratio of turns, so the voltage doubles. But the second transformer has a 1:2 ratio, so the voltage is halved again. Therefore, the end result is the same as the original voltage.
120 V
240 V
120 V
What is the voltage across the lightbulb?
1) 30 V
2) 60 V
3) 120 V
4) 240 V
5) 480 V

## Slide 33: Question 223.45.4
1) 1/4 A
2) 1/2 A
3) 1 A
4) 2 A
5) 5 A
Given that the intermediate current is 1 A, what is the current through the lightbulb?
1 A
120 V
240 V
120 V

## Slide 34: Question 223.45.4
Power in = Power out
240 V  1 A = 120 V  ???
The unknown current is 2 A.
1) 1/4 A
2) 1/2 A
3) 1 A
4) 2 A
5) 5 A
Given that the intermediate current is 1 A, what is the current through the lightbulb?
1 A
120 V
240 V
120 V

## Slide 35: Question 223.45.5
1) greater than 6 V
2) 6 V
3) less than 6 V
4) zero
A 6 V battery is connected to one side of a transformer. Compared to the voltage drop across coil A, the voltage across coil B is:
A
B
6 V

## Slide 36: Question 223.45.5
The voltage across B is zero. Only a changing magnetic flux induces an EMF. Batteries can only provide DC current.
1) greater than 6 V
2) 6 V
3) less than 6 V
4) zero
A
B
6 V
A 6 V battery is connected to one side of a transformer. Compared to the voltage drop across coil A, the voltage across coil B is:

## Slide 37: Question 223.45.10
Is there a physical justification that we know of that says the field equations must be symmetric?
Yes
No

## Slide 39
+
v
F

## Slide 40: END